## Slide 1
Causal and Non-Causal Systems
Does the output depend on the past, present or future input?
Presented by
Meet Ghelani (12502060601011)
Harshvardhan Mayani (125020606012)
Guided by
Dr. Hitesh Shah Sir
Notes: Introduce the topic, both presenters and the guide.

## Slide 2
Definitions: Causal, Non-Causal & Anti-Causal
Classify a system by checking whether its output uses past, present, or future input values.
System type | Definition | Input used | 
Causal | Output at time n depends only on present and/or past inputs. | Present + past | 
Non-causal | Output at time n depends on at least one future input. | Past/present and/or future | 
Anti-causal | Output depends only on future input values. | Future only | 
Remember: y(n) = x(n + k) → k ≤ 0 : Causal | k > 0 : Non-causal
Notes: Explain each case. Past and present dependence give causal systems; any dependence on the future makes the system non-causal.

## Slide 3
Examples: Classifying Systems
One fully solved example, then two more examples of different types.
Solved example: y(n) = x(n−1) + x(n+2)
Step 1: Take a sample value, n = 0.
Step 2: Substitute: y(0) = x(−1) + x(2).
Step 3: x(−1) is a past input, but x(2) is a future input (2 > 0).
Step 4: The output at n = 0 needs the input at n = 2, which is in the future.
Answer: Non-causal
System | Input dependence | Classification | Reason
y(n) = 3x(n) + x(n−1) | Present + past | Causal | Indices n and n−1 are both ≤ n.
y(n) = x(n+3) | Future only | Anti-causal | Uses only future input, since n+3 > n.
Notes: Solve the first example step by step on the slide using n = 0 (non-causal). Then go through the two table examples: one causal (present + past) and one anti-causal (future input only).

## Slide 4
Example for Audience
Decide: causal or non-causal?
Q1 y(n) = x(n) + x(n-2)
Q2 y(n) = x(n+3)
Q3 y(n) = x(-n)
Q4 y(n) = x(n)²
Notes: Give 1 minute per question. Answers: 1 causal, 2 non-causal, 3 non-causal (n = -1 needs x(1)), 4 causal.

## Slide 5
Applications
Real-time systems
Audio effects, control systems and sensors must be causal
Image processing
Non-causal filters use neighboring pixels for blur and edges
Offline signal analysis
ECG and speech smoothing on recorded data
Filter design
Ideal filters are non-causal; we approximate them with causal ones
Notes: Link each application to causal or non-causal use.

## Slide 6
Thank You
Meet Ghelani (12502060601011) | Harshvardhan Mayani (125020606012)
Guided by Dr. Hitesh Shah Sir
Notes: Thank the audience and guide. Invite questions.